## Slide 1: Description & Implementation of the ACMI Component
A Hardware Accelerator for the Vision Transformer Algorithm using MinHash to Lineage assignment by ENICS Lab Final Project - Computer Engineering, BIU
Noam Diamant & Itay Goldberg Academic Supervisor : Prof. Leonid Yavits Instructor : Itay Merlin August, 2024

## Slide 2: Introduction
The Goal - Lineage assignment, identifying and categorizing the lineage or variant of the COVID-19 virus.
The Method – ViTAL, A NN-based algorithm proposed as an accurate and efficient solution.
Our Focus - MinHash, technique used to estimate the similarity between two sets efficiently. A preprocessing step that feature extraction of the DNA (FASTA files).

## Slide 3: Background - MinHash
Goal - Approximate the similarity between two datasets
Assumption - probability of two sets have the same minimum hash value is equivalent to their Jaccard similarity.
Jaccard similarity measures the proportion of shared elements between two sets

## Slide 4: Background - MinHash
We will activate a uniform Hash function
We will get an estimate of the Jaccard similarity.
Instead of calculating the entire genome in this way, we select the K signatures with the lowest value for expansion and processing in a neural network

## Slide 5: Background - MinHash

## Slide 6: Existing Solutions
UShER :
Places new samples on an existing phylogenetic tree
More effective at higher coverage levels (4x and above)
Kraken2:
Uses k-mer matching for classification
Relies on exact k-mer matching, which can be problematic for erroneous DNA reads
Less effective at distinguishing between closely related SARS-CoV-2 lineages
Performance decreases significantly at lower coverage levels

## Slide 7: Comparing accuracy as a function of coverage

## Slide 8: Properties of the ACMI-accelerator
System/Configuration | Time to Place Single Genome | Speedup vs UShER | Memory Usage
ACMI-accelerated ViRAL | 2.81 ms | 69.4× | Not specified
GPU-accelerated ViRAL (RTX 2080 Ti) | 54.79 ms* | 3.53× | ~5 GB
Software-only ViRAL (Intel i7-9700K) | 94.42 ms* | 2.06× | ~3.74GB
Kraken2 | 104 ms | 1.8× | ~3.7GB
UShER | 195 ms | 1× | ~0.5 GB**

## Slide 9: ACMI implementation

## Slide 10: Hasher

## Slide 11: Hasher

## Slide 12: Sorter

## Slide 13: Sorter

## Slide 14: Kmer Buffer

## Slide 15: Kmer Buffer

## Slide 16: Index Counter

## Slide 17: Index Counter

## Slide 18: Fragment Memory

## Slide 19: Fragment Memory

## Slide 20: Fragment Memory

## Slide 21: Extender

## Slide 22: Extender

## Slide 23: Extender

## Slide 24: Synthesis
Area

## Slide 25: Synthesis
in2reg
reg2out

## Slide 26
reg2reg

## Slide 27: Summary